Elements to be covered by the Procedure:

1. Planning and Preparation

- Have spill kit in place it should include absorbent materials, drain cover, personal protective equipment: gloves, coverall, safety glasses. Refer to links for suggestions http://spilldepot.com/content/spill-response-kit

- Have a written procedure related to spill response posted at the fuel storage tank location

- Employees responding to spills needs to receive proper training including: procedure, material, personal protective equipment, hazards and limitation, proper hazardous waste disposal, reporting requirements

2. Response Procedures for Fuel Spill

- Prevent the oil from leaving the building, spreading to adjacent areas, or entering drains by absorbing flowing fuel, diking the area, and/or using drain plugs/barriers.

- Take action to stop the spill if it is continuing (i.e. shutting off valves etc.)

- Take action to prevent the spill from entering sewers or streams and to minimize the area affected. Such actions might consist of absorbing flowing oil or diking the area with sand bags, elastomer mats, or elastomer berms, etc.

If it is safe to do so:

- Spread absorbents over the surface of the spill working from the perimeter of the spill to its center.

- Socks and pillows work best on pooled liquid while pads have an advantage on thin layers of oil.

- Containerize spill residues (i.e. contaminated socks, pads, Oil Sorb, etc.) and tag for disposal as hazardous waste (disposal can be arranged through the UBC Environmental Services Facility, contact 604-822-1285 for details).

Contact UBC Risk Management Services at 604 822-2029 and the Fire Department HazMat Team (by dialing ‘911’) if:

- The quantity of spilled oil is 25 gallons or larger, or

- The spill has entered a sanitary or storm drain, or

- The spill has entered a ground or surface water, or

- The spill cannot be contained or stopped, or

- The spill poses a fire/explosion hazard, or

- Additional spill equipment is needed and is not immediately available.

In these cases of emergency spill, the person discovering it should and remain in the vicinity but at a safe distance until released by emergency responders.