Fuel Over- Fill Protection Procedure

- Person responsible for transferring the fuel to a storage tank system shall take all reasonable steps to prevent spills.

- Ensure there is enough room in the tank BEFORE each delivery. MEASURE the fuel level in the tank before the delivery;

- Monitor all fuel deliveries from beginning to end

- (Print a fuel “Inventory Report” )

- Place the fuel absorbent material and Spill Kit, at the fill site.

- When the truck arrives:

a. One employee will be present during the fill procedure

b. Verify fuel type (Diesel)

c. Verify fuel quantity

d. (Review the fuel analysis sheet verifying the fuel meets ASTA/ASTM standards)

e. Verify safe working environment:

i. Fuel delivery personnel connects the ground strap to eliminate spark

ii. Equipment in good repair – no visible cracks, tears, etc.

iii. Snug fit of all connections

- When a tank vehicle is being unloaded, the vehicle operator shall remain:

  - in constant view of the fill pipe; and

  - in constant attendance at the delivery control valve

- Upon completion:

  - (Print an “Inventory Increase Report” to verify fuel delivery )

  - (Sign the Fuel Delivery ticket from the fuel vendor )

  - Verify removal of vendor equipment

  - Return fuel spill absorbent material and Spill Kit